## Slide 1
AixSense Team
SensUs 2018
Supervisor: Dr. Sven Ingebrandt

## Slide 2
Outline
2 von 20
Initial research and Literature review
Concept Planning
Prototyping Requirements & Challenges

## Slide 3
Introduction
2 von 20
Weekly meetings with Experts and supervisor to follow-up on the development
Discussing the necessary steps and possible challenges in designing a micro-sensor
Training and learning to use the various laboratories and software to develop and build our sensor

## Slide 4
Research & literature Review
Literature review for methods of target molecule measurement
  Molecularly Imprinted Polymers, MIPS vs. antibodies
    Pros and cons
    Basis of comparison
      Measuring sensitivity, measuring time, reliability and reproducibility
      MIPS selected as the method of measurement

## Slide 5
Research & literature Review
Literature review for methods of electromechanical signal measurement
  Impedance Spectroscopy as the method of signal acquisition
    Sweep at frequency range with a known potential or current
    Calculating and plotting the impedance
Why spectroscopy?
  Distinguish between multiple electrochemical reactions
  Provide information about the capacitive changes in the system
  Changes related to the reaction of target molecule at the surface of the microsensor

## Slide 6
Concept Planning
Met with experts in the fields of biosensors to discuss the feasibility of different ideas
Experts in Microfluidics, biosensors, micro sensor design
Experts provided us with insight into what is necessary to build various sensor components
Sensor structure, functionality was discussed during previous meetings and a prototype of the sensor design is being developed

## Slide 7
Design Breakdown
Sensor based on an array of 5 inter digitated electrodes, IDE
These electrodes will be covered by the sensing area, which contains of MIPS
There will be two fluidics channels which guide the target molecule to the sensing area
Sensor is encapsulated in a protective layer to avoid performance degradation
(Someone please as the hand drawn pictures we had somewhere :D)

## Slide 8
Future Tasks
Tasks currently in team Agenda
Timetable to design a sensor on software and
Identifying the parts which are needed to be ordered
Please complete this also (:D)